## Slide 1
Lab Book 1.0. Waveguides
Student:

## Slide 2: Instructions General
SCRIPTS
From GitHub 
  Fork the repo: https://github.com/cccanvas-upv/cifoin-lab1.git
  Clone the repo using VSCode
Run the Jupyter Notebook:
  WAVEGUIDES_Student.ipynb
h
(height)
W (width)
Core
Cladding
W (width)
Core
Cladding
Slab
h_slab
h_core
shallow waveguide
deep waveguide

## Slide 3: Learning outcome #1 – Effective index of a waveguide
INSTRUCTOR:
Present Python and GDSFactory: materials, output, results.
Explain how to run a simulation for a particular cross-section.
Showcase how to change between shallow and deep waveguide.
Describe how to change the wavelength and width for the waveguide analysis.
Describe the outputs.
ALL EXAMPLE #1: waveguide width 1.2 µm, deep wvg, wavelength start and end same 1.55 µm  all ”Run”
ALL: Follow instructor, that will show how to 1) plot mode, 2) explore the results (neff …)
Document all your results (neff, plot fields of different modes, comparison between different polarizations…)

## Slide 4: Índice de refracción de los materiales silicon (Si), silicon nitride (SiNx) and silicon dioxide (SiO2)
Crystalline Silicon
Silicon Nitride

## Slide 5: Índice de refracción de los materiales silicon (Si), silicon nitride (SiNx) and silicon dioxide (SiO2)
Podemos observer como, al aumentar la longitude de onda, el índice efectivo se reduce para los 3 materiales. Esto ocurre porque __________________. Además, observamos que los índices de los materiales son, comparándolos unos con otros, mayores para el Si, de un valor intermedio para SiNx y más bajos para el SiO2.
Silicon dioxide

## Slide 6: Definición de la Cross-Section Wavelength 1.55 µm – width 1.2 µm - height 300 nm
Deep waveguide
Shallow waveguide
Las imágenes representan el índice efectivo de la sección cruzada de una guía deep y una shallow. Para ello, modificamos el parámetro slab, que hace referencia a ___________. Se observa que el shallow tiene más material no “taladrado”, y por ello tiene más material con ese índice efectivo, cercano al 2.

## Slide 7: Simulaciones – Resultados numéricos Neff y modos TE y TM para la sección cruzada de la guía deep
Neff = array([1.60524792+0.00010066j, 1.52829803+0.00017753j, 1.45072999+0.00019228j, 1.43325817+0.00021838j])
Modos TE => array([0.99505426, 0.01004259, 0.96264794, 0.047651 ])
Modos TM => array([0.00494574, 0.98995741, 0.03735206, 0.952349 ])
Observando la parte real de los índices efectivos, y teniendo en cuenta que el material del núcleo es de 2 aproximadamente, y el de la cubierta es de 1,45 aproximadamente, se puede observar que los tres primeros modos están confinados (quizás haría falta un estudio más exhaustivo para comprobar el tercer modo) y el último modo no está confinado. A su vez, Mirando los modos TE y TM se observa que el primer y tercer modo es TE y el Segundo y el cuarto es TM

## Slide 8: Field Plots
Mode 0
Mode 1
Mode 2
Mode 3

## Slide 9: Learning outcome #2 – Wavelength behavior Wavelength 1.5-1.6 µm (step 0.01 µm) – width 1.2 µm
Comment results (neff changes this way with wavelength, comparison between different waveguide cross-sections …etc)
slab = 150nm

## Slide 10: Learning outcome #3 – Width dependence Width 0.6 - 1.6 µm (step 0.1 µm) – Wavelength 1.55 µm
Comment results (neff changes this way with width, polarization behavior, etc…)

## Slide 11: Learning outcome #4 – Waveguide compact model - Find the compact models of the following waveguides: Deep waveguide, h=300nm, w=1.2um
Deep waveguide, TE0: D=-1.0060120000002706e-09, ng=1.9399937599999997
Deep waveguide, TM0: D=-1.5895973333331998e-09, ng= 1.7721028700000003
Comment on the results found for the TE0 and TM0 for both deep and shallow waveguides.
slab: 150nm

## Slide 12: Learning outcome #4 – Waveguide compact model - Find the compact models of the following waveguides: Shallow waveguide, core h=300nm, slab h=150 nm, w = 1.2um
Shallow waveguide, TE0: D=-2.4676000000548957e-11, ng= 2.0261068
Shallow waveguide, TM0: D=1.0540000000188358e-11, ng= 2.0381183000000007
Comment on the results found for the TE0 and TM0 for both deep and shallow waveguides.
slab: 150nm

## Slide 13: Learning outcome #5 – Bend waveguide radius vs. loss – deep Find neff_TE0 for wvl 1.55 µm, width 1.2 µm for R=25,50,75,100, 125,150 µm
Comment results, which is the safe radius?, consider safe means less than 0.1 dB/90º.
deep waveguide
Paste Total Loss (dB/90º) vs R & neff_TE0 vs R

## Slide 14: Thank you